## Slide 1: Object Detection of PPE used on Construction Site using YOLOv3 and Transfer Learning
Under the guidance of
Prof. Venkata Santosh Kumar Delhi
By
Sankarlal R
(Roll No. 173040063)
M.Tech Project Presentaion
on
Construction Technology and Management
Department of Civil Engineering
IIT Bombay

## Slide 2: Computer Vision
Field that works on enabling computers to see and visually sense the world around them in the same way that human vision does
Concerned with the automatic extraction, analysis and understanding of useful information from a single image or a sequence of images
Ref: https://www.shutterstock.com/video/clip-33521560-autonomous-driverless-car-computer-vision-object-detection

## Slide 3: Computer Vision in Construction Management
Fundamental requirements for collecting information at a construction site using computer-vision technology are to
  recognize workers
  construction equipment
  materials in image data
Computer vision has attracted much attention because it can provide visual information over a large area at relatively low cost and is simple to use.
Ref: https://medium.com/reconstruct-inc/what-ai-can-do-for-progress-monitoring-b47526fece5f
Notes: Visible spectrum-based imaging approaches (conventional RGB)
Simultaneous Localization and Mapping (SLAM) technique to estimate real-time positions and orientations of the robot
photogrammetry-based approach
Deep Thermal Imaging:
Proximate Material Type Recognition in the Wild through Deep Learning of Spatial Surface Temperature Patterns

## Slide 4: Safety in Construction
As per Occupational Safety and Health Administration (OSHA) report
  approximately 1 in 10 workers is injured on job site every year
In Great Britain € 14.9 billion is the estimated cost of injuries and ill health from current working conditions (HSE statistics 2016/17)
Ref: http://www.hse.gov.uk/statistics/overall/hssh1617.pdf
Cynthia L Roth (2011)
In current world scenario, it is infeasible for dedicated safety experts to visit each site
Where as computer vision engines can enhance and assure better safety standards and robust implementation at optimal cost
Notes: Visible spectrum-based imaging approaches (conventional RGB)
Simultaneous Localization and Mapping (SLAM) technique to estimate real-time positions and orientations of the robot
photogrammetry-based approach
Deep Thermal Imaging:
Proximate Material Type Recognition in the Wild through Deep Learning of Spatial Surface Temperature Patterns

## Slide 5: Research Gap
Currently networks are implemented to identify hardhat & Jacket as two objects
In the developed Model
  Uses a faster network
  Single bounding box is drawn for a person predicting the person to be safe / unsafe
  provides with a decision instead of just detection
New features considering old Models
  Saving NOTSAFE instances to date wise folders
  Date wise report generation
Ref: https://www.youtube.com/watch?v=PvPzmHLi_i0

## Slide 6: Objective
Detection of Personal Protective Equipment (PPE) used in construction industry to ensure proper usage of PPE
Develop Convolutional Neural Network (CNN) model by applying Transfer Learning to You Only Look Once (YOLOv3) algorithm
Generate date-wise report of Unsafe personnel found on site with image, date and timestamp.
Image Processing
Object Detection
Bounding Box Drawing
YOLOv3

## Slide 7: Neural Network
Ref: http://www.free-powerpoint-templates-design.com
https://homes.cs.washington.edu/~bornholt/post/nnsmt.html
https://depositphotos.com/33233003/stock-photo-robot-is-resting-and- watching.html
Program based on the way brain works
It’s a cat
It’s a cat

## Slide 8: Convolutional Neural Network
Most commonly applied to analyse visual imagery
A CNN consists of an input and an output layer, as well as multiple hidden layers.
The hidden layers of a CNN typically consist of
  Convolutional layers
  Pooling layers
  Fully connected layers
Ref: https://sushscience.wordpress.com/2016/12/04/understanding-alexnet/
Matthew D. Zeiler and Rob Fergus (2013)

## Slide 9: Convolutional Layer
3 | 0 | 1 | 2 | 7 | 4
1 | 5 | 8 | 9 | 3 | 1
2 | 7 | 2 | 5 | 1 | 3
0 | 1 | 3 | 1 | 7 | 8
4 | 2 | 1 | 6 | 2 | 8
2 | 4 | 5 | 2 | 3 | 9
1 | 0 | -1
1 | 0 | -1
1 | 0 | -1
Ref: https://slideplayer.com/slide/6242102/
FILTER
*
INPUT
OUTPUT
-5 | -4 |  | 
-5 |  |  | 
3*1 + 0*0 + 1*-1 +
1*1 + 5*0 + 8*-1 +
2*1 + 7*0 + 2*-1 = -5
-5 | -4 | 0 | 8
-10 | -2 | 2 | 3
0 | -2 | -4 | -7
-3 | -2 | -3 | -16
0*1 + 1*0 + 2*-1 +
5*1 + 8*0 + 9*-1 +
7*1 + 2*0 + 5*-1 = -4
Convolution operation
Convolution operation

## Slide 10: YOLOv3
106 convolutional layers
Darknet-53 used as feature extractor
Predictions done in 3 scales
Uses Multi-label classification
Ref: www.cyberailab.com/home/a-closer-look-at-yolov3

## Slide 11: Transfer Learning
Ref: https://blog.acolyer.org/2017/02/27/understanding-generalisation-and-transfer-learning-in-deep-neural-networks/
Stores knowledge gained while solving one problem
Apply it to a different but related problem
Person
Car
Bag
Dog
Cat
Person
Hardhat
Jacket
Andrew N G (2016)

## Slide 12: Network Modifications
Train-Validation split introduced to training model
Training code modified to save trained models and checkpoints in a folder with corresponding training date in the folder name
Modifications in evaluation code :
  Batch processing of all images in a folder and save output in same folder
  Alarm added if predicted class is NOTSAFE
  Image saving if predicted class is NOTSAFE
New code introduced to generate report
Notes: Concatenation – skip connection

## Slide 13: Data Set Preparation
Data Collection
  Manual Collection
    Videos of Construction activity taken from site, converted to images by frame capture
    Images collected: 260
  Web Scraping
    Automated web search & downloading of images
    Images collected : 1500
  Total number of Images collected: 1760
Data Augmentation
  Augmentations
    Image flipping
    30 degree clockwise rotation
    30 degree anticlockwise rotation
  Final Dataset has 2509 images

## Slide 14: Data Set Preparation
Image Labelling
  Using labelImg-master
Train, Validation & Test Set
 | Train | Validation | Test
No. of Images | 2217 | 238 | 54

## Slide 15: Training
Initial model file created by combining cfg file & weights file
Classes
Adam optimizer with initial learning rate of 0.001
Learning rate reduction by a factor of 0.1 if validation loss stops improving
Early stopping: stops training when validation loss stops improving
NOTSAFE
NoHardhat
NoJacket
SAFE
Notes: Learning rate reduction: 3 epochs
Early stopping: 10 epochs

## Slide 16: Training
 | Stage 1 | Stage 2 | Stage 3
No. of epochs (before / after unfreezing all layers) | 500 / 500 | 50 / 50 | 50 / 50
Batch Size (before / after unfreezing all layers) | 8 / 4 | 4 / 2 | 4 / 2
Epoch at which training stopped | 509 | 92 | 70
Time taken | 9d 13h 55m 20s | 3d 11h 51m 45s | 2d 5h 8m 7s
Initial Loss | 6486 | 21.88 | 12.87
Final Loss | 21.88 | 12.87 | 12.06
Notes: 10 layers freezed
Train = 277 batches, 554 batches
Val = 59 batches, 119 batches

## Slide 17: Training

## Slide 18: Working Model
Image Processing
Object Detection
Bounding Box Drawing
INPUT
OUTPUT 1: Predictions saved to Images Folder itself / new video file created with bounding boxes
YOLOv3
Images / Frames

## Slide 19: Working Model
Python code to generate report
OUTPUT 1
OUTPUT 2: NOTSAFE predictions saved to date-wise folder
OUTPUT 3: Date-wise Report of UNSAFE predictions
Triggers Alarm for 5 sec

## Slide 20: Performance Evaluation
Performance measuring Parameters
Accuracy : Correctness of class prediction
Precision : Given a class prediction from the model, how likely is to be correct
Recall : Given a class, will the model detect it correctly
F1 score : Harmonic mean of precision and recall
Accuracy
Precision
Recall
F1 score

## Slide 21: Performance Evaluation
Time taken for prediction:
  Images : 4-6 s
  Video frame rate: 2 FPS
 | Validation Dataset | Test Dataset | New Dataset
Accuracy | 0.96 | 0.96 | 0.96
Avg. Precision | 0.96 | 0.97 | 0.98
Avg. Recall | 0.96 | 0.97 | 0.95
Avg. F1 score | 0.96 | 0.97 | 0.96

## Slide 22: Predictions

## Slide 23: Predictions

## Slide 24: Limitations
Image gets saved after detecting each NOTSAFE class in single image
Person standing behind reinforcement bars not identified
Interprets blue / white cap as hardhat

## Slide 25: Conclusion
Model has a Final Loss of 12.06
Model has an Accuracy of 0.97 and Average F1 score of 0.97 on the test data set
Model is predicting with an Accuracy of 0.96 and Average F1 score of 0.96 on the new data set
Hence the Model can be used on commercial basis for safety precautions
Final loss and Accuracy can be improved by training with more images

## Slide 26: References
Joseph Redmon and Ali Farhadi, “YOLOv3: An Incremental Improvement”, 2018
Joseph Redmon and Ali Farhadi, “YOLO9000: Better, Faster, Stronger”, 2016
Joseph Redmon, Santosh Divvala, Ross Girshick and Ali Farhadi, “You Only Look Once: Unified, Real-Time Object Detection”, 2016
YOLO: Real-Time Object Detection, https://pjreddie.com/darknet/yolo/, Accessed on 23 October 2018, 9:00 hrs
What’s new in YOLO v3?, https://towardsdatascience.com/yolo-v3-object-detection-53fb7d3bfe6b, Accessed on 23 October 2018, 10:00 hrs
Ian Goodfellow, Yoshua Bengio, and Aaron Courville, “Deep Learning”, MIT Press, 2016
Matthew D. Zeiler and Rob Fergus, “Visualizing and Understanding Convolutional Networks”, 2013
Karanbir Chahal and Kuntal Dey, “A survey of Modern Object Detection Literature using Deep Learning”, 2018
Cynthia L Roth, Health and Safety: Hard Hats Guide, https://www.hsimagazine.com/article/head-protection-82, 2011, Accessed on 18 October 2018, 16:00 hrs
Health and safety statistics 2016/17, http://www.hse.gov.uk/statistics, Accessed on 24 October 2018, 16:00 hrs
Alex Krizhevsky, Ilya Sutskever, and Geoffrey E Hinton, “ImageNet Classification with Deep Convolutional Neural Networks”, 2012

## Slide 27: References
Ali Sharif Razavian, Hossein Azizpour, Josephine Sullivan, and Stefan Carlsson, “CNN Features off-the-shelf: an Astounding Baseline for Recognition”, 2014
Olga Russakovsky et al., “ImageNet Large Scale Visual Recognition Challenge”, 2014
Li Wan, Matthew Zeiler, Sixin Zhang, Yann Le Cun, and Rob Fergus, “Regularization of Neural Networks using DropConnect”, Proceedings of the 30th International Conference on Machine Learning, 2013
PASCAL2 Network of Excellence, Pascal VOC, http://host.robots.ox.ac.uk/pascal/VOC/, Accessed: 10-10-2018
A.Y. Ng, “Feature selection, l1 vs l2 regularization, and rotational invariance”, Proceedings of the twenty-first international conference on Machine learning, 2004
Twan van Laarhoven, “L2 Regularization versus Batch and Weight Normalization”, 2017
Nitish Srivastava, Geoffrey E. Hinton, Alex Krizhevsky, Ilya Sutskever, and Ruslan Salakhutdinov, “Dropout: a simple way to prevent neural networks from overfitting”, Journal of Machine Learning Research, 2014
Activation Functions: Neural Networks, Sigmoid, tanh, Softmax, ReLU, Leaky ReLU explained, https://towardsdatascience.com/activation-functions-neural-networks-1cbd9f8d91d6, Accessed: 10-10-2018
Andrej Karpathy. CS231n Convolutional Neural Networks for Visual Recognition. http://cs231n.github.io/convolutionalnetworks/, Accessed: 1-10-2018
Andrew Ng, “Course on Deep Learning Specialization”, Deeplearning.ai, Coursera

## Slide 28: Thank You !

## Slide 30: Residual Block

## Slide 31: How Neural Network works ?
Input = X
Output , Y =A2
: True Label
W, B : Weight & Bias
g : Activation function
Z1 = + B1
A1 = g(Z1)
Z2 = + B2
A2 = g(Z2)
Forward Pass
Back Propagation
Logistic regression Loss,
L = - ( log Y + (1-)log (1-Y))
dW2 =
dB2 =
W2 : = W2 – dW2
B2 : = B2 – dB2
dW1 =
dB1 =
W1 : = W1 – dW1
B1 : = B1 – dB1
Gradient Descent optimization
If relu activation,
A = max (0,Z)

## Slide 32: Optimization Algorithm
Decides how weight gets updated
Gradient Descent: w := w – α dw, where α is the learning rate
Adam optimizer combines Gradient Descent with Momentum & RMS prop algorithms
Momentum: + (1-) dw
RMS prop: + (1-
Adam: w := w – α
Where & are bias corrected values
Bias correction: = , t is the epoch number
          = , t is the epoch number
=

## Slide 33: Train – Val – Test split
 |  | Train Set | Validation Set | Test Set
Number of Images |  | 2217 | 238 | 54
Data Points Per Class | NOTSAFE | 882 | 96 | 19
 | NoHardhat | 779 | 72 | 17
 | NoJacket | 970 | 112 | 23
 | SAFE | 1040 | 115 | 27

## Slide 34: Why YOLOv3 ?
In YOLO Object detection framed as a regression problem
Whole detection pipeline is a single network
  Can be optimized end-to-end directly on detection performance
Predicts boxes at three different scales
  Good resolution spatial information on object locations
Shows significant improvement in detecting small objects
Extremely fast
Working Machine: Titan X
(GPU with 12 GB RAM)
Joseph Redmon and Ali Farhadi, 2018
Notes: mean average precision is the metric to measure the accuracy of object detectors
floating point operations per second is a measure of computer performance,
Frames per second is frequency at which consecutive images called frames appear on a display.

## Slide 35: Error Message while training

## Slide 36: Performance Evaluation
 |  | HUMAN |  |  | 
 |  | NOTSAFE | NoHardhat | NoJacket | SAFE
MODEL | NOTSAFE | 19 | 0 | 1 | 0
 | NoHartdhat | 0 | 17 | 0 | 0
 | NoJacket | 0 | 0 | 21 | 1
 | SAFE | 0 | 0 | 1 | 26
Confusion Matrix (Test set)
True Positive (TP)
True Negative (TN)
False Positive (FP)
  For NOTSAFE Class
False Negative (FN)
  For NOTSAFE Class
Accuracy =
Precision =
Recall =
F1 score =

## Slide 37: How YOLO does object detection?
Joseph Redmon, Santosh Divvala, Ross Girshick and Ali Farhadi (2016)
Input image split into SXS grid
Create bounding boxes & predicts confidence for each box
Predict class probability for each cell
Multiply confidence value and class probability
Choose best prediction using Non maximal suppression
Notes: P(object), P(Class ! Object)
Confidence score- how confident the model is that the box contains an object and how accurate it thinks the box is that it predicts
For PASCAL VOC dataset
YOLO – 24 Conv layers, 2 FC layers,
7X7 grid,
2 bounding boxes for each cell
5 parameters
20 classes
7*7*(2*5+20) = 1470 parameters that the net predicts

## Slide 38: Why Transfer learning ?
Higher start.
  The initial skill (before refining the model) on the source model is higher than it otherwise would be.
Higher slope.
  The rate of improvement of skill during training of the source model is steeper than it otherwise would be.
Higher asymptote.
  The converged skill of the trained model is better than it otherwise would be.
With TL
Without TL
Ref: https://machinelearningmastery.com/transfer-learning-for-deep-learning//

## Slide 39: System Configuration
OpenCV
Hardware
  CPU: Intel Core i7-4790@3.60GHz *8
  RAM: 8GB 1600MHz
  Intel HD Graphics GPU
Environment
Ubuntu 16.04
Python
Tensorflow
PIP
Keras
Atom
LabelImg-master
Operating System
Programming Language
Package Management System
Computer Vision Library
Computational Framework
DL Framework
Image Annotation Tool
Text Editor
Notes: application programming interface (set of communication commands)
Ubuntu is a free and open-source operating system and Linux distribution based on Debian
Python is an interpreted high-level programming language
pip is a package management system used to install and manage software packages written in Python
OpenCV is a library of programming functions mainly aimed at real-time computer vision
TensorFlow is an computational framework, object detection api
Keras is a high-level neural networks API, written in Python and capable of running on top of TensorFlow, CNTK, or TheanoThe Jupyter Notebook is an open-source web application that allows you to create and share documents that contain live code, equations, visualizations and narrative text

## Slide 40: Previous Classifiers
Sliding window (VGGNet, Inception)
Region Proposals: First predict which parts of the image contain interesting information
In both approaches, we need to run the classifier many times

## Slide 41: Pooling Layer
Max Pooling
Average Pooling
1 | 3 | 2 | 1
2 | 9 | 1 | 1
1 | 3 | 2 | 3
5 | 6 | 1 | 2
FILTER: 2X2
INPUT
9 | 9 | 2
9 | 9 | 3
6 | 6 | 3
Max Operator
OUTPUT
9 |  | 
Maximum
Maximum
9 | 9 | 
1 | 3 | 2 | 1
2 | 9 | 1 | 1
1 | 3 | 2 | 3
5 | 6 | 1 | 2
FILTER: 2X2
Stride: 2
3.75 | 1.25
4 | 2
Average Operator
OUTPUT
3.75 | 
Average
Average
3.75 | 1.25
INPUT

## Slide 42: Fully Connected Layer
Ref: https://medium.com/reconstruct-inc/what-ai-can-do-for-progress-monitoring-b47526fece5f
Neurons in a FC layer have connections to all activations in the previous layer
High-level reasoning in the neural network is done here
Looks at what high level features most strongly correlate to a particular class and has particular weights
when we compute the products between the weights and the previous layer, we get the correct probabilities for the different classes
Notes: if the program is predicting that some image is a bird, it will have high values in the activation maps that represent high level features like wings or a beak, etc

## Slide 43: Learning in Layers
First layers learn to identify simple lines and shapes
Second layer is more complex which naturally follows from the non-linearity between layers
This pattern for from all layers, more complex patterns are constructed as we reach the top layers in the CNN.
Ref: http://bmia.bmt.tue.nl/people/BRomeny/Courses/Taipei2017/index.html
Andrew N G (2016)

## Slide 44: Non Maximal Suppression
Many bounding boxes for one object
Box with highest confidence selected
For remaining boxes, If IoU > 0.5, bounding box discarded
https://www.pyimagesearch.com/2016/11/07/intersection-over-union-iou-for-object-detection/
Andrew N G (2016)